## Slide 1
Production Preparation Process (3P) Workshop
Notes: NOTE: This module can be used after the 3P Kick-Off Event Presentation or as a stand alone event.
The three-day 3P Kick-off Event introduces 3P as a concept, selects the product or process to be 3P’d and establishes the baseline data and the requirements for the 3P Lab and sets up the Project Charter.
If the project is small enough or the team is experienced in 3P, then this Workshop presentation can be used without a 3P Kick-off event providing the Project Charter has been specified beforehand and adequate preparations have been made to run the Workshop including having a 3P Lab available.

## Slide 2
Other Modules In This Series:
5S
Standard Work
Total Productive Maintenance (TPM)
Administrative Lean
Cell Design/ Production Preparation Process (3P)
Kaizen
Kanban
Problem Solving
Poka Yoke Quality Systems
Transaction Process Improvement (TPI)
Cause & Effect Diagram with the Additions of Cards (CEDAC)
Single Minute Exchange of Dies (SMED)
Value Stream Mapping (VSMi®)
Visual Management
Managing Daily Process Excellence
For More Information Please Contact:
Mark DeLuzio, President and CEO
+1.860.234.0915
mark.deluzio@leanhorizons.com
Strategically Creating Value Through the Elimination of Waste

## Slide 3
This document contains confidential and proprietary information owned by Lean Horizons Consulting, LLC. Any disclosure, use, copying or distribution of this information without the express written consent of Lean Horizons Consulting is strictly prohibited.

## Slide 4: Ground Rules for Event
Safety first (use personal protective equipment)
Active participation by all
Start and end on time
All electronic gadgets (phones, pagers, etc) turned to “off” or “silent”
Computers to be used only when instructed
Keep an open mind to change
Don’t let “perfect” get in the way of “better”
Notes: DO: Perform Group Introductions. Or Take two minutes to learn about another person and then 1 minute to present them to the group e.g. name, where were they born, where do they live now, family – married, children, hobbies, personal qualities, position, career, what do they like about work, what do they expect to get from this event.
Pick an ice-breaker or exercise to warm the team up to the event. (Icebreaker Example: Everyone uses their name tent and writes a “Personal License Plate” in which they have 2 minutes to creatively use a total of 7 letters or numbers to tell us something about themselves. Examples “LV2SAIL” OR “DADOV5”
DO: Review Event Ground Rules.
ASK: “Does anyone have any rules they would like to see added?”
ASK: “Does everyone agree to these?”

## Slide 5: 3P Exercise: Part 1
Simulate a 3P exercise.
Objective
Instructions
Form teams of 3-7 participants. Each team will be given 10 sheets of paper.
Each member of the team is to draw at least three alternative designs of a paper airplane that will fly for at least 2 seconds from a height of 5’ (1.5m) and that also looks aesthetically pleasing. The key criteria is that the plane can be made quickly and consistently.
Each team is to select the best three designs and construct a prototype of each, test the prototypes against the above criteria and then agree on the final model.
Time to Complete
Deliverable
20 minutes
Consensus final design paper airplane
Notes: SAY: “3P is largely a creative thinking event. Teams are challenged to keep the creative juices flowing as we strive to achieve breakthrough designs and processes. So it is appropriate that we kick the event off with a 3P style creative, team-building exercise. This is a competitive exercise and teams are competing against each other.”
MATERIALS REQUIRED: 1 stopwatch as many sheets of 8.5x11” (or A4) paper per team as required. (Optional: Colored pencils)
DO: Read the instructions aloud with the class on the slide. Have the materials prepared and the tables already assembled to facilitate working in small groups.
DO: Encourage the teams to think about how things in nature achieve flight. Birds, flying squirrels, air borne seeds etc.
DO: Ensure that they follow the 3P process of: i) individual drawn designs, ii) selecting the top three, iii) prototyping and then iv) final selection on the one best solution. Also ensure it is clear that they have 20 minutes in their teams to come up with their final airplane design and test it.
NOTE: Allow the class to come up with their own method for how to determine the best design. Do not be too directive here. Also you may be asked what the criteria for “aesthetically pleasing” is. Just say that “it must look like an airplane or other type of aircraft (no floating flat pieces of paper!)”. Either select a “Customer” or you act as Customer and be the ultimate judge. The Customer can not participate in the team exercises.

## Slide 6: 3P Exercise: Part 2
Simulate production of the consensus design from the previous exercise.
Objective
Instructions
In the same teams, you will be given 15 minutes to plan production and forecast how many paper airplanes your team can build in a 2 minute period and how much profit you can make.
Costs = $1 for each sheet of paper, $10 for each team member and $5 for each reject airplane.
Income = $5 per completed plane (approved by customer)
At the end of the production run count your finished airplanes and calculate your profit. Planes must be of the same quality as the prototype and fly for 2 seconds.
Time to Complete
Deliverable
30-45 minutes
All results compared and winning team announced.
Discuss lessons learned
Notes: DO: Read aloud the instructions on the slide for Part 2. Ensure all teams understand they are to build as many of their chosen design of airplane in 2 minutes as they can.
DO: Provide 15 minutes for each team to plan and test their production method and forecast how many paper airplanes the team can build in a 2-minute period and how much profit they will make. Costs and income are indicated on the slide. Write their forecasts on a flip chart or board.
DO: Ensure they understand that the planes must be of the same quality as the prototype and will be examined upon completion by the customer (Observer).
DO: Run the production exercise for 2-minutes. The Customer should be keeping time and taking notes. When the production run is completed, the Customer must inspect the planes to be the same quality as the prototype and remove any inferior planes. Remember to keep a tally of these for later when calculating costs.
DO: Ask each team in turn to select one member to fly each plane from approximately 5’ (1.5m) height. The Customer decides if the plane has passed the 2-second test and failed planes are again deducted from the final count.
DO: Score the teams using the following table, compare the profits and identify the winning team.
SCORE TABLE
Team Predicted Profit Total # Produced # Rejects Final Profit
Team 1
Team 2
etc
DISCUSSION QUESTIONS TO ASK:
Was the final result different from the forecast? Why?
Was there any conflict in the group?
Did certain people take on or accept roles within the team?
Was quality a concern?
Did everyone participate in the discussion and decision-making process?
DO: Relate how we will see elements of this exercise in our 3P event.

## Slide 7: Goal of 3P
Develop and implement a new product/process with the highest quality, lowest cost, in the shortest time
Apply learning to next 3P
Leadership Awareness/ Commitment
PROCESS STEP 1
3P Kick-Off
PROCESS STEP 2
3P Workshop
PROCESS STEP 3
Implement
PROCESS STEP 4
Notes: DO: Introduce the notion of Deming’s PDCA in relation to 3P as an iterative process of creative divergence and constructive convergence and refinement.
This Introduction is a review of 3P to remind delegates of what was covered in the Kick-off presentation or, if experienced in 3P, to revise and reorient them.

## Slide 8: 3P Roadmap to Success
Apply learning to next 3P
Leadership Awareness/ Commitment
PROCESS STEP 1
3P Kick-Off
PROCESS STEP 2
3P Workshop
PROCESS STEP 3
Implement
PROCESS STEP 4
Attend 3P Executive Overview
Readiness Assessment
Prerequisites
Commitment to 3P process
3P Overview Training
Define the requirements
Create 3P Lab
Prepare Event Charter & Plan
Detailed 3P Training and Exercises
Application of 3P Methodology to Design/Process
Creation of Implementation Plan
Plan equipment, fixtures, tooling
Develop support systems
Install and qualify
Create Standard Work

## Slide 9: 3P Roadmap to Success
Apply learning to next 3P
Leadership Awareness/ Commitment
PROCESS STEP 1
3P Kick-Off
PROCESS STEP 2
3P Workshop
PROCESS STEP 3
Implement
PROCESS STEP 4
Develop Plan to Implement
Build, Present, and Select Process Prototypes
Sketch and Evaluate Alternative Process Steps
Study and Analyze Examples from Nature, etc.
Define Objectives/ Needs

## Slide 10: 3P Workshop Structure
Develop Plan to Implement
Build, Present, and Select Process Prototypes
Sketch and Evaluate Alternative Process Steps
Study and Analyze Examples from Nature, etc.
Define Objectives/ Needs
Identify Voice of the Customer and current performance metrics
Select target, write charter, pick the team
Review product
Define key functions
Find examples from Nature, etc.
Define 16 Catch Phrases
Sketch 7 Alternatives for each process step
Apply 16 Catch Phrases
Evaluate and Combine
Plan equipment, fixtures, tooling
Plan support systems
Prepare implementation plan
Present
Prototype Top 3 Alternatives
Refine & Evaluate
Scale up Top Alternative

## Slide 11: 3P Workshop Agenda
Day | Key Learnings | Daily Deliverables
1 | Process Analysis Key Functions | Process diagram
2 | Back to basics/Nature 16 Catch Phrases | Function Sketches 7 Alternatives (for each process step)
3 | Visual Creativity Selection Criteria | Evaluate 7 Mockup
4 | Physical Limits/Interfaces Duration & Effort | Refine & Combine/Select Top 1 Process @ Glance Implementation Plan
5 | Prepare for Team Final Report-Out | Final Report-Out to Management
Notes: NOTE: Make any modifications or inclusions/deletions to Workshop event as required by nature of 3P event.

## Slide 12: 3P Defined
Production Preparation Process (3P) is a team approach to concurrent production process and product design that delivers:
  Highest customer Quality
  At the lowest product and capital Cost
  With better Safety, Ergonomics and Less Environmental Impact
  For the required Volume
  Able to Flex to volume changes
  On Time and in the shortest project Lead Time

## Slide 13: 3P Defined
3P is an advanced lean tool typically used by organizations that have experience with other lean methods
3P focuses on eliminating waste by building quality into the process through product and process design
3P starts with a clean product development slate to rapidly create and test potential product and process designs that require the least time, material, and capital resources
3P involves a diverse team in a multi-day creative process to identify several alternative ways to meet the customer's needs
Notes: SAY: “3P is an advanced lean tool typically used by organizations that have experience with other lean methods
Kaizen and other lean tools take a production process as a given and seek to make improvements, 3P focuses on eliminating waste through product and process design.
3P seeks to meet customer requirements by starting with a clean product development slate to rapidly create and test potential product and process designs that require the least time, material, and capital resources.
3P involves a diverse group of individuals in a multi-day creative process to identify several alternative ways to meet the customer's needs using different product or process designs.
Eliminate the ‘Three D’s’ – dirt, difficult, dangerous”

## Slide 14: Goal of 3P
Least waste by integrating the ‘4M’s’ (Man, Material, Machine, Methods) of production into a good flow
Eliminate Muda (waste), Mura (variability), Muri (overloading)
Eliminate the ‘Three D’s’ – dirt, difficult, dangerous
Build quality into the process with Poka-yoke & Jidoka

## Slide 15: When to use 3P – Top 5 Reasons
New product development. Educate designers in Lean as early as possible.
Capital expenditure approval. Don't sign a Cap Ex without first doing 3P.
Product design changes. Don’t approve changes without a 3P review.
Significant changes in volume. If you didn't design the process Lean, here's a second chance.
Relocation of processes. If you're going to pick it up and move it anyway, you might as well Lean it out first.

## Slide 16: Benefits
Increased sales – extended product life cycle, early adopters increased early stage pricing
First to market – increase chances of competitor lock-out
Enhance market image as innovative producer
Improved product performance
Reduced production cost – product and capital required
Reduced development costs
Increases profitability
Notes: SAY: “Product performance can be enhanced in two ways; 1) by involving multidisciplinary teams early, an improved solution can be found, 2) by having a fast development process, development can afford to wait for improved or cheaper technology and still make it to market on time.
Lower production costs do not naturally follow as typically 2X effort leads to ½ development time. However more focused effort and fewer iterations and mistakes can lead to improved development efficiency and lower development costs.”

## Slide 17: Prerequisites for successful 3P
Organizational lean maturity
Strategic alignment and VOC
Follow kaizen guidelines
Cross-functional associate involvement
Adequate mechanical and design capabilities
Establish 3P Lab with supplies and staff
Leadership sponsorship
Willingness to be revolutionary

## Slide 18: Obstacles to Product Development
Chaotic work environment – constant interruptions
Resources spread too thinly – resource bottlenecks
Failure to prioritize projects/tasks
Poor communication and lack of multi-disciplinary team approach
Poorly defined product requirements and constant changes
Lack of a formal design process with checkpoints
Late consideration of manufacturability
Lack of effort in concept development and evaluation

## Slide 19: 3P Principles – overarching logic of 3P
Kaikaku - rapid revolutionary, not incremental evolutionary change
Cross-functional team based creative design
Moonshine: sketch, model, simulate, prototype, scale up
Diverge then converge, then repeat
Catch Ball and refine
Design in quality, design out waste

## Slide 20: The Four Phases of 3P
VOC/spec’s
Part Numbers
Drawings
Samples
Standards
Interfaces
Volumes
Ramp
Takt Time
Process Steps
Target Costs
7 Alternatives
16 Catchphrases
Simulations
Model Lab
Selection
Flow Chart
Takt Time
Cycle Time
Equipment Plan
Process Capacity
Standard Work
Standard Layout
Launch Phase
Information Phase
Creative Phase
Definition Phase
3P Kickoff
3P Event
3P Implementation
Notes: SAY:”3P is an iterative process of creative divergence and constructive convergence and refinement through four phases: Information, Creative, Definition and Launch.”

## Slide 21: Product and Production Interaction
A. Product Planning
B. Function Definition
C. Product Alternatives
D. Refine and Test
E. Detail Design
9. Volume Production
8. Process Pilot
7. Equipment Procurement
4. Trials: Design & Process
6. Equipment Planning
5. Detail Production Process
3. Refine and Test
2. Process Alternatives
1. Production Planning
Constant Interaction Between Paths
10. Installation
11. Service
12. End of Life
Notes: SAY: “This is a Concurrent Engineering method and is to illustrate that product design and production design need to run hand in hand with constant interaction between the two. This is very relevant to 3P. The traditional method is to design the product in isolation and throw it over the wall to the production department to make the best of it. Often product designers do not understand manufacturing and vice versa.”
SAY: “It is the interaction of product designers and production engineers that will achieve the best possible solution when using the 3P method.”

## Slide 22: 5 Steps to 3P
Define Product/Process Design Objectives/Needs
Study Alternatives by Diagramming and Finding and Analyze Examples from Nature or other sources
Sketch and Evaluate Alternative Process Steps
Build, Present, and Select Process Prototypes
Develop Implementation Plans
Notes: 3P FIVE STEP CREATIVE PROCESS
1. Define Product or Process Design Objectives/Needs
The team seeks to understand the core customer needs that need to be met. If a product or product prototype is available, the project team breaks it down into component parts and raw materials to assess the function that each plays.
2. Study Alternatives
Diagramming: A fishbone diagram or other type of illustration is created to demonstrate the flow from raw material to finished product. The project team then analyzes each branch of the diagram (or each illustration) and brainstorms key words (e.g., roll, rotate, form, bend) to describe the change (or “transformation”) made at each branch.
Find and Analyze Examples in Nature: The project team then tries to find examples of each process keyword in the natural world. For example, forming can be found in nature when a heavy animal such as an elephant walks on mud, or when water pressure shapes rocks in a river. Similar examples are grouped and examples that best exemplify the process key word researched to better understand how the examples occur in nature. Here, team members place heavy emphasis on how nature works in the example and why. Once the unique qualities of the natural process are dissected, team members then discuss how the natural process can be applied to the given manufacturing process step.
An alternative comparison method is to ask how other industries solve similar problems. e.g. how food processing companies eliminate contamination to reduce mix to mix contamination in other processing industries or how Automotive companies solve similar problems found in the Aerospace industry and visa versa.
3. Sketch and Evaluate the Process
Sub-teams are formed and each sub-team member is required to draw different ways to accomplish the process in question. Each of the sketches is evaluated and the best is chosen (along with any good features from the sketches that are not chosen) for a mock-up.
4. Build, Present, and Select Process Prototypes
The team prototypes and then evaluates the chosen process, spending several days (if necessary) working with different variations of the mock-up to ensure it will meet criteria.
Hold Design Review: Once a concept has been selected for additional refinement, it is presented to a larger group (including the original product designers) for feedback.
5. Develop Project Implementation Plan
If the project is selected to proceed, the team selects a project implementation leader who helps determine the schedule, process, resource requirements, and distribution of responsibilities for completion.

## Slide 23: 3P Process
1 – Leadership 3P Awareness | 2 – Select target area and team | 3 – Collect data
4 – Train Team | 5 – Design Criteria | 6 – 3P Lab

## Slide 24: 3P Process
7 – Each team member individually draws 7 Alternatives. | 8 – Team gathers to group and evaluate ideas. Selects the top 7. | 9 – Team moonshines the 7 Alternatives.
10 – Team evaluates each Alternative. Selects the top 3. | 11 – Team moonshines the top 3 Alternatives. | 12 – Team selects Top Alternative.
3
1
7
7
7
7
7
7
7
7

## Slide 25: 3P Process
13 – Team refines Top Alternative. | 14 – Team completes Process At A Glance form for Top Alternative | 15 – Team prepares Implementation Plan.
16 – Present to Leadership. | 17 – Select builder & prepare fixture and tooling drawings. | 18 – Install, qualify, ramp up.
Key Actions

## Slide 26: Define Needs and Objectives
Objectives:
Review team charter and pre-event data collection
Complete Muda walk and observation of current process/design
Complete “before” video and take digital photos
List issues for safety, ergonomics, quality, delivery, cost
Review results of interviews with key personnel
Brainstorm and complete Affinity Diagram process
Plan to Implement
Prototype
Sketch and Evaluate Alternatives
Examples from Nature etc.
Needs and Objectives
Notes: DO: Review chapter objectives.
NOTE: Defining Needs and Objectives is covered in detail in the 3P Kick-off event. This slide is a review of that information or if this is a stand alone event this information can be collected now.

## Slide 27: Exercise: Review Team Charter
As a team, review the event charter.
Objective
Instructions
Review the event charter and validate event objectives and project boundaries.
Time to Complete
Deliverable
20 minutes
Make any necessary modifications to charter.
Needs and Objectives

## Slide 28: What is “Waste”?
Types of Waste | Descriptions
1. Muda | Any activity that consumes resources without creating value for the customer
2. Mura | Unevenness in a process; for example an uneven work pace causing people to hurry and wait
3. Muri | Overburdening, overloading, or stressing of resources (such as people or equipment)
Needs and Objectives
Notes: DO: Explain the three types of waste that originate from the Japanese.

## Slide 29: The Content of Work
Needs and Objectives
Value Added Work - maximize
  The part of the job the customer values
Enabling Waste - minimize
  Work that does not add value but is necessary under the current operating conditions
Obvious Waste - eliminate
  Work that does not add value and is not necessary
Notes: NOTE: A simple exercise to illustrate this slide is to use a use a pen to mark a small 1” circle on a board or flipchart.
SAY: “Let’s pretend that a customer orders a circle.”
Start by fetching the pen from a few paces away.
Pull the cap off and draw a circle.
ASK: ”What is Value Added?” Ans.=Drawing the circle (emphasis that that is what the customer ordered and is willing to pay for)
ASK: “What is Obvious waste?” Ans.=Walking to fetch the pen.
ASK: “What is Enabling waste?” Ans.=Taking the cap off (necessary because pen would dry out if not replaced)

## Slide 30: The Eight Wastes Defined
Wastes | Definition
Defects | Process steps that result in scrap, rework or re-processing.
2. Over Production | Producing more product than is required at the current time.
3. Waiting | Periods of inactivity while waiting for the next process step to begin.
4. Non-Utilized Talent | Unused creativity and underutilized human capital.
5. Transportation | Product moving from person to person or between locations.
6. Inventory | Unprocessed or partially processed materials, or undelivered finished goods.
7. Motion | Excessive movement by people or machines.
8. Extra Processing | Unnecessary work beyond what is required to meet customer requirements.
Needs and Objectives
Notes: Mnemonics: DOWNTIME
DO: Ask the class to provide examples of the 8 wastes. Capture their answers on a chart paper. The participants can write the answers in their workbooks.

## Slide 31: Muda Walk Observation
Examine waste closely
Independently collect examples
Compare notes
Prioritize
Save for comparison to design alternatives
Needs and Objectives

## Slide 32: Example Data to Review
Ramp schedule
Delivery peak volume
Scalability (volume fluctuations)
Takt time
Replenishment times
Standard WIP
Layouts and people
QFD or Strategic Deployment
Process steps or maps
Value Stream Map
Part Numbers
Drawings
Samples
Time: process time, lead time and value added time
Changeover times
Typical batch sizes
Quality (process outputs)
Number of Poka Yokes
Reliability
Cost Targets
Needs and Objectives

## Slide 33: Review VOC
A detailed understanding of the customer’s requirements
A common language for the team going forward
Key input for the setting of appropriate design specifications for the new product or service
A highly useful springboard for product & process innovation.
Needs and Objectives

## Slide 34: Review results of interviews regarding current process/design
Operators
Supervisors
Inspectors
Managers
Material Handlers
Maintenance
Tech Support
Needs and Objectives

## Slide 35: Complete Affinity Process
Make visible the problems we have learned about in this data review
Needs and Objectives
Notes: SAY: “Notice the time on the clock, that’s 6:35pm – just getting started.”

## Slide 36: Exercise: Take Muda Walk
As a team, observe the process, dissect the product
Objective
Instructions
Complete Muda Walk and observation of current process or design
Observe and document repetitive builds (multi-cycle analysis)
Complete Motion Analysis (Eliminate, Combine, Modify, Simplify)
Complete “Before” Video
Interview stakeholders
Complete Affinity Diagram of all opportunities
Time to Complete
Deliverable
Provided by facilitator
List issues observed for safety, ergonomics, quality, delivery, cost.
Complete the Affinity Diagram.
Needs and Objectives

## Slide 37: Exercise: Management Review
Management review of conclusions from the data and finalized charter
Objective
Instructions
Management review of conclusions from the data and finalized charter
Time to Complete
Deliverable
20 minutes
Approval of charter and event direction.
Needs and Objectives

## Slide 38: Complete Diagram of the Current Process/Design
Objectives:
Decide on diagram(s) format
Complete diagram process
Review decision matrix and adjust criteria accordingly
Identify and rank opportunities
Summarize key opportunities
Assign sub-teams to begin 3P cycles
Plan to Implement
Prototype
Sketch and Evaluate Alternatives
Examples from Nature etc.
Needs and Objectives
Notes: DO: Review chapter objectives.

## Slide 39: Diagrams
Points | Descriptions
Fishbone Diagram | 4 M’s: Man, Material, Method, Machine
Process Fishbone | Sequence of build with components, and processes
Exploded Assemble | Illustration of all assemblies
Design Diagram | The whole system
Process Map | The whole system or sub-process
Needs and Objectives

## Slide 40: Process Fishbone Diagram Example
Needs and Objectives

## Slide 41: Exploded Assembly
Use drawings and exploded views to visualize product or process
Needs and Objectives

## Slide 42: Process 3P Diagram Example
Needs and Objectives
Operation
From:
STANDARD WORK SHEET
Part No.
Sequence
To:
Part Name:
Quality Check
Safety Precaution
Standard WIP
# Pieces WIP
TAKT Time
Cycle Time
+
Raw Material
Assembly
123-A
Bracket
Mill
Drill
Tap
Grind
Assembly
Test
Pack
Raw
Material
Finished
Goods
+
+
+
+
1
2
3
4
5
7
6
4
77”
70”

## Slide 43: Value Stream Map and Process Map
Needs and Objectives
High-level snapshot of end-to-end business
Used to identify where opportunities for improvement exist
Does not incorporate decision loops
VALUE STREAM MAP
Detailed graphical depiction of a manufacturing or business process
Used to identify specific improvements
Incorporates decision loops within the process
Notes: SAY: “A Value Stream Map is the “30,000-foot” view of the process. A Process Map is a tool that would take just one process box from a Value Stream Map, and explode that process into it’s detailed steps.”

## Slide 44: Example Process Mapping Symbols
Needs and Objectives
Operation
A Step in the process
that adds value.
Measurement
To inspect, verify, count,
examine, gage for quality
or quantity.
Transportation
To move from one place to
another. (Not part of an
operation or inspection.
Transmission
To send information by
electronic means.
Storage
To hold for later use. (I.e., in a queue).
Decision
A step in the process where
a change in the flow may
occur.
Delay
To wait for the next operation.
(I.e., in a queue).
No value added.

## Slide 45: Break into manageable projects
Complex products and processes may need to be segmented due to limitations in current technology, space, cost, ‘laws of nature’
Might initially focus on final assembly, then later look at components
3P Design Team needs to revisit the Charter and make any adjustments to scope and prioritize sequence
Risk of sub-optimization – need to Catch Ball up and down stream
Needs and Objectives

## Slide 46: Prioritize Opportunities
Needs and Objectives
Prepare a Decision or Pugh Matrix; adjust criteria & weightings
Rank impact, effort, complexity risk
Or, dot vote or other method to identify greatest opportunities

## Slide 47: Summarize key opportunities
Prioritize which process steps or components need the most work
Create sub-teams to begin 3P cycles on the prioritized process steps and components
Needs and Objectives

## Slide 48: Exercise: Diagrams
Complete diagram process to identify and prioritize opportunities.
Objective
Instructions
As a team, determine which diagram(s) best suits the project and complete the diagram(s). Rank and prioritize 3P opportunities.
Determine 3P sub-teams and assign 3P projects to the sub-teams.
Determine # of 3P cycles needed for event.
Time to Complete
Deliverable
Provided by facilitator
Completed diagrams indicating focus priorities.
Needs and Objectives

## Slide 49: 3P Creative Thinking Process
Objectives:
Identify key functions of the assignments from the diagram
Identify key words that describe each function
Brainstorm and draw examples from nature or other source of each function
Group like ideas
Present final ideas
Plan to Implement
Prototype
Sketch and Evaluate Alternatives
Examples from Nature etc.
Needs and Objectives
Notes: DO: Review chapter objectives.

## Slide 50: 3P Cycle
Each team member individually draws 7 Alternatives. | Team gathers to group and evaluate ideas. Selects the top 7. | Team moonshines the 7 Alternatives.
Team evaluates each Alternative. Selects the top 3. | Team moonshines the top 3 Alternatives. | Team selects Top Alternative.
3
1
7
7
7
7
7
7
7
7
Examples from Nature

## Slide 51: Thinking Outside The Box
Stimulate the team to think laterally about solutions.
Objective
Instructions
Given the handout “Join the Dots”, follow the instructions to join all the dots with the number of lines stated.
Time to Complete
Deliverable
10 minutes
Review how this has parallels to creative design.
Examples from Nature
Notes: DO: Either print out copies of the three Dot Puzzles in Join-the-Dots.ppt or use blank paper and get the participants to make their own Dot matrices and solve the puzzles.
Show the first slide of Join-the-Dots.ppt and then give the participants 2 minutes to try to join the dots with the required number of consecutive lines. For the first one this is 4 lines.
Then reveal the answer. Reinforce the idea of thinking outside the ‘self limiting’ box in order to get a solution.
Then show them the 12 Dot puzzle and ask them to complete it with 5 lines.
Reveal the answer and then repeat for the 16 dot puzzle.
Finally show the alternative solution to the 9 dot matrix at the end.

## Slide 52: Identify key functions
Examples from Nature
Determine the key functions of the process to be studied from the diagram(s)

## Slide 53: Identify key words for each function
Examples from Nature
KEY WORDS
Guide
Turn
Drill
Roll
Clamp
Rigidity
Shear
Swivel
Fasten
Spin
Brake
Slide
Oscillate
Press
Lock
Bond

## Slide 54: Exercise: Determine Function
Determine key functions.
Objective
Instructions
Using the example provided on the following page, determine the key functions for the product.
Answer: how does it add value to the customer?
Determine customer needs.
Time to Complete
Deliverable
15 minutes
Report out key functions, value added, and customer needs.
Examples from Nature

## Slide 55: Define Function Exercise
Examples from Nature
How would you describe the product: Styrofoam cup
What does it do? Name the features or characteristics. How does it add value to the customer? List the customer needs.
Verb-Noun Functions
Notes: NOTE: Features include: convex interior, ridge for stacking, base, cup walls
Functions include: hold liquid, stack cup, insulate liquid, lift base, etc

## Slide 56: Back to Nature Examples
Examples from Nature
Nature has spent millions of years refining these phenomena
Spin
Separate
Crawl
Shear
Adhere
Encapsulate
Cling
Buoy
Hinge
Move
Attach
Grip

## Slide 57: TRIZ – 40 Principles
Examples from Nature
Rushing through
Blessing in disguise
Feedback
Intermediary/Mediator
Self-Service
Copying
Cheap short-living objects
Replacement of mechanical system
Pneumatics and hydraulics
Flexible membranes and thin films
Porous materials
Color change
Homogeneity
Discarding and Recovering
Parameter Change
Phase transition
Thermal expansion
Accelerated oxidation
Inert atmosphere
Composite materials
Segmentation
Taking out or extraction
Local quality
Asymmetry
Merging / Consolidation
Universality
Nested doll
Anti-weight
Prior counteraction
Prior action
Cushion in advance
Equipotentiality
The other way round
Spheroidality – Curvature
Dynamics
Partial or excessive action
Another dimension
Mechanical vibration
Periodic action
Continuity of useful action
Select key words and features from the 40 Principles
Notes: DO: Pass out TRIZ Handout.
SAY: “TRIZ is a Russian acronym for “The theory of Inventive Problem Solving”
Developed by G Altshuller et al from studying over 400,000 patents and how inventors solved problems.
Read handout on Triz 40 Inventive Principles.dot with examples and explanations.
Use the Contradiction Matrix.xls to help select which principles to use.

## Slide 58: Other Solution Sources
Examples from Nature
Study the way others have solved things and list the key words for each function
Competitors
  Copy, adapt and improve
Other industries
  Food vs. process
  Auto vs. Aero
Pattern Breaking tools
  Reverse assumptions, forcing associations, making comparisons, other points of view, blue sky

## Slide 59: Exercise: Creative Thinking
Begin the 3P Creative Thinking Process.
Objective
Instructions
In the sub-teams, complete the following activities:
Identify Functions from the diagrammed opportunities
Identify Key Words and principles for each Function
Each team member draws 7 examples of each key word or principle as found in nature or other
Present and group like examples with sub-team.
Report final results to rest of class.
Time to Complete
Deliverable
Provided by facilitator
Report out results from creative thinking exercise.
Examples from Nature
Notes: SAY: “Why 7? The answer I was given is “because 6 is too few and 8 is too many” from my Japanese Sensei!”

## Slide 60: 16 Catch Phrases of 3P
Objectives:
Identify the purpose of the 16 Catch Phrases
Define each of the 16 Catch Phrases
Review the Muda Walk Worksheet
Capture examples and non-examples of the 16 Catch Phrases
Plan to Implement
Prototype
Sketch and Evaluate Alternatives
Examples from Nature etc.
Needs and Objectives
Notes: DO: Review chapter objectives.

## Slide 61: Purpose of 16 Catch Phrases of 3P
Sketch and Evaluate Alternatives
The 16 Catch Phrases of 3P are used as guidelines for designing processes according to Lean manufacturing principles of Takt, Flow, Pull, and Jidoka.

## Slide 62: 16 Catch Phrases
Eliminate wasted machine cycle time
Build equipment for small, swift flow lines
Use short, vertical flow lines
Build equipment for one-piece pull
Build in quick changeover
Link machines for smooth loading and unloading
Use multiple lines & untangled flows
Spiral upwards to Jidoka
Production preparation should be lightning fast
Build & layout equipment for smooth material flow
Use additive equipment
Build products and equipment that is easy to set up
Make equipment easy to move
Use multi-purpose equipment
Make operator work stations narrow
Layout equipment for ease of operator movement
Sketch and Evaluate Alternatives
Notes: 1. Production preparation should be lightning fast. Avoid over planning, use what you have, act now. 2. Build & layout equipment for smooth material flow. Flow like a river, not like a dam. 3. Use additive equipment. Buy many speedboats instead of one tanker. 4. Build products and equipment that is easy to set up. Design in the separation of internal and external tasks. 5. Make equipment easy to move. No roots, no vines, no pits. Put wheels on everything. 6. Use multi-purpose equipment. Simple, "just fast enough" machines that perform one function well. 7. Make operator work stations narrow. Town houses, not ranch houses. 8. Layout equipment for ease of operator movement. Remove obstruction to smooth human motion. 9. Eliminate wasted machine cycle time. Design out 'air cutting' and minimize machine movements. 10. Build equipment for small, swift flow lines. Enable Standard Work (Takt, Work Sequence, SWIP). 11. Use short, vertical flow lines. Vertical = advancing process flow, horizontal = functional. 12. Build equipment for one-piece pull. Machine level. This is probably the most critical one. 13. Build in quick changeover. Design in SMED at the machine level. 14. Link machines for smooth loading and unloading. Line stops when WIP on the line is "full work". 15. Use multiple lines & rectified flows. 'Rectified' is an odd term, electrical engineers will get it. 16. Spiral upwards to Jidoka. There are 5 steps to Jidoka, which should be pursued a step at a time.

## Slide 63: 1. Production Preparation should be lightning fast
Sketch and Evaluate Alternatives
From Concept to Production
Avoid over planning, use what you have, act now

## Slide 64: 2. Build & layout equipment for smooth material flow
Sketch and Evaluate Alternatives
Use Lean Flow techniques – no waste, cells, Kanban Flow like a river, not like a dam

## Slide 65: 3. Use additive equipment
Sketch and Evaluate Alternatives
Buy many speedboats instead of one tanker

## Slide 66: 4. Build equipment that is easy to set up
Sketch and Evaluate Alternatives
Design in the separation of internal and external tasks
Change-over Flowing gap
Old product
New product
5
4
3
2
A
5
4
3
2
B
1
1
5
4
C
2
1
5
3
D
2
1
3
E
2
4
1
3
F
2
4
5
Notes: NOTE: This principle refers to building lines and equipment that can produce multiple products with minimal setting-up.
Also products can be designed to minimize set-up time, such as standard hole sizes, to fit same jig etc.
Use the principles of SMED to remove as much set-up work as possible to be external to the machine cycle. Any set-up work inside the cycle time is internal time.

## Slide 67: 5. Make equipment easy to move
Sketch and Evaluate Alternatives
No roots, no vines, no pits, put wheels on everything
Notes: SAY: “Don’t fasten things down, make it easy to move things.
Don’t have fixed service locations and lots of wires and pipes. Use flexible pick-ups, short wire runs and make it ‘plug and play’.
Don’t put machines in pits, buy machines that stand flat and can be moved.”

## Slide 68: 6. Use multi-purpose equipment
Sketch and Evaluate Alternatives
Simple, "just fast enough" machines that perform one function well
Gem Core Drivematic, Cost $297,000
3P ‘Moonshine’, Cost $7,300

## Slide 69: 7. Make operator work stations narrow
Sketch and Evaluate Alternatives
Ranch style - Wide and Shallow
Townhouse – Narrow but Deep
Reduced Walking
1step - station to station
Principle of Verticality
Reduced Footprint
U-Line
Fishbone Line
Town houses, not ranch houses
Notes: SAY: “Principle of verticality means select machines that have a small footprint but may be tall.”

## Slide 70: 8. Layout equipment for ease of operator movement
Sketch and Evaluate Alternatives
Can change manning to suit demand.
Remove obstruction to smooth human motion
Fixed Layout
Flexible Layout

## Slide 71: 9. Eliminate wasted machine cycle time
Sketch and Evaluate Alternatives
Design out 'air cutting' and minimize machine movements
Switch on drill press
Air cutting down (Muda)
Drilling
Air cutting up (Muda) Only the hole is value added

## Slide 72: 10. Build equipment for small swift flow lines
Sketch and Evaluate Alternatives
Enable Standard Work (Takt, Work Sequence, SWIP)
Notes: SAY: “These two lines perform the same functions. The right hand line can be moved, rearranged, flexibly manned and reused for other product lines if required.”

## Slide 73: 11. Use short, vertical flow lines
Sketch and Evaluate Alternatives
Horizontal = functional
Forming
Stores
Painting
Assembly
Welding
Machining
Inspection
Vertical = advancing process flow
Inspect
Machine
Weld
Paint
Assemble
Store
Inspect
Form
Weld
Assemble
Paint
Store
Machine
Weld
Form
Paint
Assemble
Store

## Slide 74: 12. Build equipment for one-piece pull
Sketch and Evaluate Alternatives
Customer and supplier are linked. Customer pulls.
Customer and supplier are not linked. Supplier pushes.
Machine level flow. This is probably the most critical one.
Notes: SAY: “The concept of push vs. pull is clear from the slide. Getting machines to do this is the trick. Machines must only produce when required and what is required, specified to be balanced for Takt time and flexible.”

## Slide 75: 13. Build in quick changeover
Sketch and Evaluate Alternatives
1
5
4
3
2
A
1
3
4
5
2
B
Flexible Cell Changes
Use standard sizes
b
a
a
Use stops or centering grooves to set positions
Pear shape holes and ‘C’ washers for quick bold release
Design in the separation of internal and external tasks – SMED
Use programmable equipment for flexible set-ups
Minimise bolt lengths
Notes: SAY: “This principle refers to making products and equipment that can be changed over quickly. Design products that are interchangeable, standard sizes so the machines do not need to be reset for each different component.
Use the principles of SMED to remove as much work as possible to be external to the machine cycle. Any work inside the cycle time is internal time.”

## Slide 76: 14. Link machines for smooth loading & unloading
Sketch and Evaluate Alternatives
Line stops when WIP on the line is "full work"
Machines unlinked with variable WIP
Machines linked with standard WIP
Notes: SAY: “This is the concept called “Chaku Chaku” in Japanese, meaning “load load”. It is an efficient style of production in which all the machines needed to make a part are situated in the correct sequence very close together. Standard WIP, cycle times and operator work can be balanced. The operator simply loads a part and moves on to the next operation. Each machine performs a different stage of production, such as turning, drilling, cleaning, testing or sandblasting.”

## Slide 77: 15. Use multiple lines & untangled flows
Sketch and Evaluate Alternatives
B1
B2
B3
B4
F1
F2
F3
F4
P1
P2
P3
P4
A1
A2
A3
A4
Model A
Model B
Model C
Model D
B1
B2
F1
F2
F3
F4
P1
A1
A2
A3
Model A
Model B
Model C
Model D
B = Blank F = Fabricate P = Paint A = Assembly
Confusing Flow
Use multiple and rectified flows
Rectified Flow

## Slide 78: 16. Spiral upwards to Jidoka
Sketch and Evaluate Alternatives
Jidoka | 
7 | Quality Check (Poka-Yoke)
6 | Part Removal (Hanedashi)
5 | Autonomation of Returns
4 | Automation of Stops
3 | Autonomation of Feed
2 | Automation of Holding
1 | Autonomation of processing
Take each step at a time, do not jump
Notes: DO: See article/blog on The 5 Steps to Building Jidoka Equipment by Jon Miller.

## Slide 79: Exercise: 16 Catch Phrases of 3P
Capture examples and non-examples of the 16 Catchphrases of 3P.
Objective
Instructions
In small groups, utilize the 16 Catch Phrase Walk form on the following page to go to the gemba and find both examples and non-examples of the 16 Catch Phrases of 3P.
Take digital pictures, upload, and report-out.
Time to Complete
Deliverable
60 minutes
Report out digital pictures to rest of class. Discuss key take-aways.
Sketch and Evaluate Alternatives

## Slide 80: 16 Catch Phrase Walk Form
Sketch and Evaluate Alternatives
1 form completed per pair/group
Use to identify both good and bad examples of the 16 Catch Phrases in the workplace

## Slide 81: 3P Design Evaluation Criteria
Objectives:
Understand importance to have the design “spec” early in the discovery process
Translate VOC, 3P data collection, stakeholder interviews in to requirements
Evaluate proposed requirements – must vs. want
List design requirements before generating alternatives
Come to group consensus
Plan to Implement
Prototype
Sketch and Evaluate Alternatives
Examples from Nature etc.
Needs and Objectives
Notes: DO: Review chapter objectives.
DO: Use the material captured in the Kick-off event if available.

## Slide 82: Design Evaluation Criteria
Typical considerations:
Safety
Environmental
Critical customer requirements
Space or other physical limitations
Budget
Timeline urgencies
Product or process regulatory qualification requirements (e.g. UL testing for consumer electronics, or PPAP for automotive)
Sketch and Evaluate Alternatives
Notes: PPAP = Production Part Approval Process

## Slide 83: 7 Alternatives Form: Product Design
Sketch and Evaluate Alternatives

## Slide 84: 7 Alternatives Form: Process Design
Sketch and Evaluate Alternatives
Notes: Toyota use checklists as a form of standard operation and as a training aid. This example is a composite extract from Toyota.

## Slide 85: Use Motion Analysis to Assist Process Selection Criteria
Sketch and Evaluate Alternatives

## Slide 86: Develop Weighting Criteria and Ranking System
Create the weighting criteria and ranking system to evaluate the 7 Alternatives
May need to include:
  VOC
  Industry Regulations
  Requirements identified from initial data collection, charter
Sketch and Evaluate Alternatives

## Slide 87: Exercise: Design Evaluation Criteria
Establish the customer and technical requirements
Objective
Instructions
As a group, identify at least 12 design requirements to help guide the creative process.
Don’t limit your thinking, just make sure all requirements are considered.
Come to group consensus by using a weighted decision matrix or multi-vote
Time to Complete
Deliverable
30 minutes
List of critical design requirements
Sketch and Evaluate Alternatives

## Slide 88: The 7 Alternatives
Objectives:
Create and draw the 7 Alternatives for each function
Review Lean Machine Checklist and modify to develop rating criteria for the 7 Alternatives
Rate each team member’s 7 Alternatives
Select final 7 Alternatives for the team
Complete the Process-At-A-Glance form for each of the 7 Alternatives
Present final 7 Alternatives
Plan to Implement
Prototype
Sketch and Evaluate Alternatives
Examples from Nature etc.
Needs and Objectives
Notes: DO: Review chapter objectives.

## Slide 89: Create and Draw the 7 Alternatives for each function
The 7 Alternatives
Sketch and Evaluate Alternatives
Use the brainstorming results from the nature etc exercise as a source of inspiration to create the 7 Alternatives for each function
Each team member initially draws 7 Alternatives for each function

## Slide 90: Example of Process Alternatives
Sketch and Evaluate Alternatives

## Slide 91: Complete Process At A Glance for 7 Alternatives
Material – show the value-added step or transformation, “what changes?”
Method –show the function of the person’s hands, “what do they do?”
Gauge – show the device used to ensure 100% quality, “how do we measure”
Tool – show actual tool that does the processing, “what makes the product feature?”
Fixture – show how the work piece is held, “what holds the part?”
Sketch and Evaluate Alternatives

## Slide 92: Process At A Glance Form
Sketch and Evaluate Alternatives

## Slide 93: Exercise: 7 Alternatives
Create and evaluate the 7 Alternatives.
Objective
Instructions
In the sub-teams, complete the following activities:
Each team member brainstorms and draws 7 Alternatives
As a sub-team develop rating criteria and ranking system for 7 Alternatives
Rate and rank each idea
Select Top 7 Alternatives
Complete Process-At-A-Glance Form for 7 Alternatives
Time to Complete
Deliverable
Provided by facilitator
Report out the final 7 Alternatives
Sketch and Evaluate Alternatives

## Slide 94: Selecting the Top 2-3 Alternatives
Objectives:
“Trystorm” each of the 7 Alternatives for each function
Review Lean Machine Checklist and modify to develop rating criteria to determine the Top 2-3 Alternatives
Rate each prototype
Select Top 2-3 Alternatives
Refine the Process-At-A-Glance form for each of Top 2-3 Alternatives
Present Top 2-3 Alternatives
Plan to Implement
Prototype
Sketch and Evaluate Alternatives
Examples from Nature etc.
Needs and Objectives
Notes: DO: Review chapter objectives.

## Slide 95: “Trystorming” Process
Like it sounds, Trystorming is a hands-on extension of brainstorming
Old adage, “If at first you don’t succeed, try, try, again.”
Trystorming is different from brainstorming in that it encourages the rapid development and test of an idea rather than merely thinking about the possible solutions.
Build up through multiple cycles: sketch, scale model (in clay or balsa wood), full scale – evaluating and adjusting (tweaking)
Prototype

## Slide 96: Sometimes called “Moonshining”
Not conventional thinking
Many people will not like it
You may have to keep it a secret from your own organization - “skunk works”
May feel uncomfortable until people come to accept it
Prototype

## Slide 97: Lean Process Machine Checklist
D-3 In-house development
D-4 Off-the shelf equipment or components
S-1 Proper guarding and safety devices in place
S-2 Dust, chips, slag, etc. collected by equipment
S-3 Not dangerous, dirty or difficult
S-4 High ergonomics evaluation score
S-5 Meets environmental, fire, and health regulations
S-6 Minimal operator training
L-1 Creates one-piece flow
L-2 Meets Takt Time
L-3 Creates a pull system
L-4 Quick set-up and changeover
L-5 Operator input
L-6 Chaku-chaku (load load)
L-7 Hanedashi (auto unload)
L-8 Mobile & flexible, on wheels, not roots or vines
Q-1 Process is low risk or known
Q-2 Poka Yoke is built into the process
Q-3 100% gauging for in-process checks
Q-4 Fewer than 0.03% defects
Q-5 Auto-stop for abnormality (jidoka)
C-1 Low motion waste
C-2 Low capital investment
C-3 Equipment is readily available
C-4 Minimal space required
C-5 Known process technology
C-6 Minimal development time required
C-7 Simpler than existing process methods
C-8 Easy autonomous maintenance, or maintenance free
C-9 High ratio of value-added time in the process
C-10 Low tooling cost
C-11 Low toolroom maintenance
D-1 Suitable for estimated volumes
D-2 Volumes easily scalable up by 400% or down to 25%
Prototype

## Slide 98: Exercise: Top 2-3 Alternatives
Complete process to down select to top 2-3 Alternatives.
Objective
Instructions
In the sub-teams, complete the following activities:
Sub-team creates prototypes for each of the 7 Alternatives
As a sub-team develop rating criteria and ranking system for Top 2-3 Alternatives
Rate and rank each prototype
Select Top 2-3 Alternatives
Refine Process-At-A-Glance for Top 2-3 Alternatives
Time to Complete
Deliverable
Provided by facilitator
Report out the Top 2-3 Alternatives
Prototype

## Slide 99: Selecting the Top Alternative
Objectives:
Continue to refine “trystorming” prototypes
Combine with other sub-teams as needed to combine ideas to create final result
Refine final Alternative and Process-At-A-Glance Form
Plan to Implement
Prototype
Sketch and Evaluate Alternatives
Examples from Nature etc.
Needs and Objectives
Notes: DO: Review chapter objectives.

## Slide 100: Exercise: Creating the Top Alternative
Complete process to down select to Top Alternative.
Objective
Instructions
In the sub-teams, complete the following activities:
Sub-team refines prototypes for top 2-3 Alternatives
Complete rating and ranking of prototypes
Combine with other sub-teams as needed to create the Top Alternative
Complete final prototype and Process At A Glance Form
Report-out to other sub-teams
Time to Complete
Deliverable
Provided by facilitator
Report out on the Final 1 Alternative to other sub-teams
Prototype

## Slide 101: Process At A Glance Form
Prototype

## Slide 102: 3P Implementation Plan
Objectives:
Create project plan
Create concepts and shop drawings for fixtures and tooling
Prepare key elements of Implementation Plan
Prepare final report-out for 3P Event
Plan to Implement
Prototype
Sketch and Evaluate Alternatives
Examples from Nature etc.
Needs and Objectives
Notes: DO: Review chapter objectives.

## Slide 103: 3P Process
13 – Team refines Top Alternative. | 14 – Team completes Process At A Glance form for Top Alternative | 15 – Team prepares Implementation Plan.
16 – Present to Leadership. | 17 – Select builder & prepare fixture and tooling drawings. | 18 – Install, qualify, ramp up.
Key Actions
Plan to Implement

## Slide 104: Create Project Plan
Develop Work Breakdown Structure
Estimate effort (direct work), duration (lapse time)
Resource list and availability
Sequence
Dependencies
Track deliverables & costs
Plan to Implement

## Slide 105: Create concepts and shop drawings for fixtures and tooling
Plan to Implement
Full Scale Top Design Prototype was built without engineering drawings, just paper and pencil sketches - now create drawings that capture the design intent
Clearly indicate key functions, tolerances, measurement points

## Slide 106: Prepare Key Elements of Implementation Plan
High level estimates and sequence of events following approval of the 3P Design
Steps:
  Design detail: tooling and fixture engineering drawings
  Equipment Plans: builder selection, acceptance criteria
  Support Systems: material handling, maintenance, information systems
  Installation: samples, qualification, standard work
  Startup: training, daily management
Plan to Implement

## Slide 107: Prepare Final Report Out and Budget
Charter
Objectives
Top Design Metrics
Implementation Plan
Benefits Summary
Plan to Implement

## Slide 108
Other Modules In This Series:
5S
Standard Work
Total Productive Maintenance (TPM)
Administrative Lean
Cell Design/ Production Preparation Process (3P)
Kaizen
Kanban
Problem Solving
Poka Yoke Quality Systems
Transaction Process Improvement (TPI)
Cause & Effect Diagram with the Additions of Cards (CEDAC)
Single Minute Exchange of Dies (SMED)
Value Stream Mapping (VSMi®)
Visual Management
Managing Daily Process Excellence
For More Information Please Contact:
Mark DeLuzio, President and CEO
+1.860.234.0915
mark.deluzio@leanhorizons.com
Strategically Creating Value Through the Elimination of Waste