## Slide 1
Cell Design

## Slide 2
Other Modules In This Series:
5S
Standard Work
Total Productive Maintenance (TPM)
Administrative Lean
Cell Design/ Production Preparation Process (3P)
Kaizen
Kanban
Problem Solving
Poka Yoke Quality Systems
Transaction Process Improvement (TPI)
Cause & Effect Diagram with the Additions of Cards (CEDAC)
Single Minute Exchange of Dies (SMED)
Value Stream Mapping (VSMi®)
Visual Management
Managing Daily Process Excellence
For More Information Please Contact:
Mark DeLuzio, President and CEO
+1.860.234.0915
mark.deluzio@leanhorizons.com
Strategically Creating Value Through the Elimination of Waste

## Slide 3
This document contains confidential and proprietary information owned by Lean Horizons Consulting, LLC. Any disclosure, use, copying or distribution of this information without the express written consent of Lean Horizons Consulting is strictly prohibited.

## Slide 4: Ground Rules for Event
Safety first (use personal protective equipment)
Active participation by all
Start and end on time
All electronic gadgets (phones, pagers, etc) turned to “off” or “silent”
Computers to be used only when instructed
Keep an open mind to change
Don’t let “perfect” get in the way of “better”
Notes: DO: Perform Group Introductions. Pick an ice-breaker or exercise to warm the team up to the event. (Icebreaker Example: Everyone uses their name tent and writes a “Personal License Plate” in which they have 2 minutes to creatively use a total of 7 letters or numbers to tell us something about themselves. Examples “LV2SAIL” OR “DADOV5”
DO: Review Event Ground Rules.
ASK: “Does anyone have any rules they would like to see added?”
ASK: “Does everyone agree to these?”

## Slide 5: Goal of Cell Design Module
To apply the principles and components of proper Cell Design to achieve a target goal for your business.
Do’s and Don’ts of Cell Design
Building Quality Into the Cell
Steps to Designing a Cell
Key Concepts of Cell Design
Notes: DO: Introduce the notion of Cell Design and the goal of this event.
SAY: “The major objectives of this module are that we want you to:
1 – Understand the key concepts of Cell Design
2 – Identify the steps to designing a cell
3 – Identify how to build quality into the cell
4 – Define what are the do’s and don’ts of Cell Design”

## Slide 6: Cellularization
An arrangement of equipment, people, machines, and methods that facilitate continuous flow production
Allows for one-piece flow whenever possible
One operator can process the entire part when needed
Usually grouped by either product family or process
Popular configuration is “U” Shaped
Notes: DO: Define for the class what we mean by a cell or a cellular arrangement.

## Slide 7: Cellularization fundamentally reduces all of the 8 wastes
Less inventory (improved quality)
Minimizes walking
Promotes better work balance (lower cost)
Enables multi-process handling
Promotes better communication
Staffing flexible as demand changes
Scheduling and manning assignments easier
Easier to manage
Benefits to Cellularization
3
1
2
5
4
6
Notes: SAY: “Cellularization both in the office and factory fundamentally reduces all of the 8 wastes.”
DO: For each of the benefits ask the group if they have an example or can explain how cellularization fulfills that benefit.

## Slide 8: Exercise: Cell Design Charter Review
Review the Cell Design Charter for the event against charter criteria
Objective
Instructions
As a team review the event charter and answer the following questions:
What is the business need for this event?
Who is the owner?
What are the goals for this event?
Time to Complete
Deliverable
30 minutes
Make any modifications to charter as necessary.
Notes: DO: Review the charter for this event.

## Slide 9: Key Concepts of Cell Design
Objectives:
Differentiate between batch production, flow production, and “fake” flow production
Review characteristics of cellular flow
  Counterclockwise flow
  Machines in close proximity
  Operator Flow vs. Part Flow
  Separate operator from machine
Define chaku-chaku and levels of automation
Do’s and Don’ts of Cell Design
Building Quality into the Cell
Steps to Designing a Cell
Key Concepts of Cell Design
Notes: DO: Review chapter objectives.

## Slide 10: One Piece Flow Production in a Cellular Layout
Significantly reduces:
  Transportation
  Inventory
  Waiting time
While improving:
  Quality
  Delivery
  Cost
Product Flow in a Cellular Plant Layout
Key Concepts of Cell Design
Wave Solder
Packing
PC Board Assembly
Final Assembly
Testing
Customer
Raw Material
Notes: DO: Define one-piece flow.

## Slide 11: Batch Production
Key Concepts of Cell Design
INVENTORY
Notes: DO: Review what is happening on the slide and what we mean by “batch production.”
ASK: “What wastes do you see on this slide with batching?”

## Slide 12: Flow Production
Key Concepts of Cell Design
Waste
CUSTOMER
RM
RM
Notes: ASK: “What wastes have been eliminated by moving to one piece flow?”

## Slide 13: Fake Flow Production
Key Concepts of Cell Design
CUSTOMER
RM
RM
Notes: ASK: “What do you see happening in this graphic?”
ASK: “Why is this not single piece flow?”

## Slide 14: Example of Cellular Flow
Key Concepts of Cell Design
Notes: ASK: “Here is a picture of a manufacturing cell. What are some characteristics that you see?”

## Slide 15: Why Counterclockwise?
Designed to pull with the right hand and then pass to the next process with the left hand
This method takes into account that the right hand is the dominant hand for most.
Cellular Flow is Typically Counterclockwise
Key Concepts of Cell Design
Reprinted with permission from BigPhotoStock.com
Notes: DO: Discuss why cellular flow is typically counterclockwise. Ask if it would make sense to ever challenge that? (answer: yes – where it makes sense to do so – with lean there are very few absolutes, you have to apply it to your situation).

## Slide 16: Machines in Close Proximity
Key Concepts of Cell Design
25’
15’
215 Pieces
Operator runs 3 machines to produce a part
Daily Production ___________
Feet per shift ___ _________
Feet Per (240 days) year ____________
Miles (5280 ft.) per year ____________
Shear
Punch
Lathe
17,200
4,128,000
782
Notes: NOTE: For a possible drawing on a chartpaper: Draw a picture with the three operations and show how the distances will be shorter in a u-shape even if the distances remain the same, the backtracking is reduced by being in a u.

## Slide 17: Cellular Flow
Operator and part follow the same sequence
Operator Flow vs. Part Flow
Key Concepts of Cell Design
5
4
3
2
1
10
9
8
7
6
R
F
Notes: SAY: “In this case, the operator and part follow the same sequence.”

## Slide 18: Cellular Flow
Operator does not flow the same as the part
Operator Cellular Flow vs. Part Flow
Key Concepts of Cell Design
2
1
3
4
3
2
1
4
5
6
4
3
2
1
R
5
6
7
8
F
Notes: SAY: “Here is another work sequence combination where the operators do not flow the same as the part. Note, Operator #1 retrieves the raw material completes steps 1,2 7,8 and deposits the finished product into the finished goods container. Operator #2 completes steps 3,4 5 & 6 in this work sequence.”

## Slide 19: Cellular Flow: Separate Operator from Machine
1 OPERATOR, MULTIPLE MACHINES
1 OPERATOR, 1 MACHINE
Key Concepts of Cell Design
Notes: SAY: “A key lean concept of cellular flow is to separate the operator from the machine.”
ASK: “What do you think we mean by this?”
SAY: “We want to remove as much non-value added activity from the operator as possible. How many people stand and watch their washing machines wash the clothes at home? We don’t do that at home, why would we want to do that at work? As much as possible we want to look for opportunities to free the operator from one machine to be able to work multiple machines/processes.”

## Slide 20: To Automate or Not to Automate?
Level | Cycle | Unload | Load | Transfer
1 | Manual | Manual | Manual | Manual
2 | Auto | Manual | Manual | Manual
3 | Auto | Auto | Manual | Manual
4 | Auto | Auto | Auto | Manual
5 | Auto | Auto | Auto | Auto
Key Concepts of Cell Design
Level 3 = Ideal State (Chaku-Chaku)
Notes: DO: Review the levels of automation and how we try to kaizen the process in this sequence.

## Slide 21: Chaku-Chaku
Means “load-load”
Operator should flow continuously from operation to operation spending less than 1-2 seconds per operation
A operator simply loads the part and moves on to the next operation
Automatic unloading of the workpiece (hanedashi)
The workpiece is oriented at unload
All operator movement in one plane (no reaching)
Key Concepts of Cell Design
Notes: DO: Define chaku-chaku.

## Slide 22: Steps to Designing a Cell
Objectives:
Identify the steps to designing a cell
Review examples of each step
Do’s and Don’ts of Cell Design
Building Quality into the Cell
Steps to Designing a Cell
Key Concepts of Cell Design
Notes: DO: Review section objectives on slide.

## Slide 23: Steps to Designing a Cell
    Determine what the cell is to produce
Create cardboard cut-outs of the cell
Identify the workstation design
Determine the tool and material presentation
Define the material replenishment procedures
Steps to Designing a Cell
Notes: DO: Provide brief overview of the steps to designing a cell.
SAY: “We will explain each of these in more depth on the upcoming slides.”

## Slide 24: Steps to Designing a Cell
    Determine what the cell is to produce
Create cardboard cut-outs of the cell
Identify the workstation design
Determine the tool and material presentation
Define the material replenishment procedures
Steps to Designing a Cell
Notes: SAY: “The first step is to determine what the cell should produce.”

## Slide 25: Determine What the Cell is to Produce
Steps to Designing a Cell
Product Family Analysis
Benefits of Product Family Matrix
A matrix tool to determine similarities of process steps and sequence.
The analysis sheet is the first step to determining what will be produced by the cell or cells
Shows model/volume relationship
Determines similarities
Can reduce the need for change-overs
Points Descriptions
1
2
Notes: SAY: “We do this by conducting a product family analysis of all of the parts that are made and the processes they go through in order to be made. We look for similarities in order to identify product families. Groups of parts then make sense to be made together in a cell.”

## Slide 26: Product Family Matrix
Steps to Designing a Cell
Product Family Matrix Example aka PQPR*
PROCESS NAME
Part #
Demand
Quantity
% of Total
CNC Mill
Center
Lathe
Grind
Roll
Clean
Gear
Teeth
Cutting
Assembly
Packaging
1
OBR-026
420
35

‚
ƒ
„
…
†
2
OBR-030
288
24

‚
ƒ
„
…
†
3
OBR-008
276
23

‚
ƒ
„
…
†
4
320147
84
7

‚
ƒ
„
…
†
5
330033
48
4

‚
ƒ
…
„
†
‡
6
330003
24
2

‚
ƒ
„
…
†
7
330030
24
2

‚
ƒ
„
…
†
8
320148
12
1

‚
ƒ
„
…
†
9
320087
12
1

‚
ƒ
„
…
†
10
OBR-004
12
1

‚
ƒ
„
…
†
TOTAL
1,200
100
Notes: DO: Review this simple example.
DO: *Explain Product Quantity Process Routing from VSM and Standard Work.

## Slide 27: Steps to Designing a Cell
    Determine what the cell is to produce
Create cardboard cut-outs of the cell
Identify the workstation design
Determine the tool and material presentation
Define the material replenishment procedures
Steps to Designing a Cell
Notes: SAY: “Step 2 is to create cardboard cut-outs of the cell.”

## Slide 28: Creating Cardboard Cut-Outs
A “footprint” of a cell using cardboard cut-outs
Benefits:
  Cell can be designed and improved many times before moving machines
  Allows visualizing of the cell layout
  Involves everyone on the team
  Allows for multiple layout ideas
Steps to Designing a Cell
Cardboard Cut-Outs
Notes: DO: Define the cardboard cut out method and ask the group what the advantages would be.

## Slide 29: Cardboard Cut-Out Method
Steps to Designing a Cell
Step 4
Select the best option
This should be a team consensus
Look at proposed design again for any problems
Step 3
In open area place “machines” in the flow you wish to try
Experiment with different layouts
Create multiple alternatives
Team-based
Watch for potential problems
Mark the operator load/unload point with red for visibility
Step 2
Each machine or process step footprint is exactly replicated in a cardboard cut-out
Full size is used so people can readily visualize magnitude
Step 1
Notes: SAY: “A few additional notes on cardboard cut-outs…
  Cut-outs may not be needed for simple “easy to move” operations.
  If possible, have the host facility prepare cut-outs prior to the Kaizen event.
  Make sure to stress that this is a team based exercise - operator involvement is critical
  Watch for potential problems (barriers, reverse flow, etc.) or physical constraints (structural beams, posts, etc.)”

## Slide 30: Example of a Cell Using Cardboard Cut-Outs
Steps to Designing a Cell
Notes: SAY: “Here is another example of a cell designed by cardboard cut-outs.”

## Slide 31: Steps to Designing a Cell
    Determine what the cell is to produce
Create cardboard cut-outs of the cell
Identify the workstation design
Determine the tool and material presentation
Define the material replenishment procedures
Steps to Designing a Cell
Notes: SAY: “Step 3 is to identify the workstation design.”

## Slide 32: Work Station Design
Size the workstation for the parts
Arrange the parts in the proper sequence and orientation
Standardize hardware and tools
Place fixtures and hand tools in order of use
Establish visual control of tools (shadow board)
Make machines fit the process
Optimize operator motions
Steps to Designing a Cell
Notes: DO: Review key points on the slide.

## Slide 33: Steps to Designing a Cell
    Determine what the cell is to produce
Create cardboard cut-outs of the cell
Identify the workstation design
Determine the tool and material presentation
Define the material replenishment procedures
Steps to Designing a Cell
Notes: SAY: “Step 4 is to determine how the tools and materials are to be presented to the cell/operator.”
ASK: “Why is this important? What benefit is there to doing this?”

## Slide 34: Tool and Material Presentation
Steps to Designing a Cell
Point of Use
Benefits of good tool & material presentation
Tools and materials located where they are needed
Operators should not have to reach, bend, or exert excess (wasted) motion to retrieve materials or tools required for an operation
Improve working ergonomics
Reduce walk time
Reduce cycle time my reducing unnecessary motion
Eliminates lost tooling
Improves safety
No searching for tools
Easier replenishment
Points Descriptions
1
2
Notes: SAY: “Appropriate space needs to be allocated for tools and materials!”

## Slide 35: Material and Tool Presentation Examples
Steps to Designing a Cell

## Slide 36: Steps to Designing a Cell
    Determine what the cell is to produce
Create cardboard cut-outs of the cell
Identify the workstation design
Determine the tool and material presentation
Define the material replenishment procedures
Steps to Designing a Cell
Notes: SAY: “Step 5 is to define the material replenishment procedures, by this we mean what is the process around bring parts to the cell and taking completed parts/products away from the cell.”

## Slide 37: Material Supply Principles
Resupply path
  Supply components from behind the line / outside the cell
Ergonomics
  No bending, stretching, twisting, or lifting
Organization of materials
  Labeled
  Assigned homes
  Arranged in order of use
  Foot printed
  Stored in only one location
Steps to Designing a Cell
Notes: SAY: “It is important to choreograph the steps and sequence to how the materials will be supplied to the cell.”

## Slide 38: Supermarkets
The supermarket is for storage
Use a water spider to supply the line
Replenish the line frequently - every hour
Remember -- it’s only an interim solution!
  The goal is to have suppliers ship just in time
Steps to Designing a Cell
Notes: DO: Define supermarkets and cover key points on the slide.

## Slide 39: Water Spider Characteristics
Steps to Designing a Cell
Benefits
Purpose
Definition
Individual(s) responsible for material replenishment to the cell(s)
Delivers in kits to the line
Delivery is JIT according to standard operations
Must utilize 5S principles to assure good visual controls
Allows operators to “operate”
  Eliminating material handling
  Searching for parts
  Walking to resupply
  Orienting parts
Improves quality by
  Establishing accountability for material presentation
  Reduces mismatches, use of wrong parts
  Manages production control
1
2
3
The role of Water Spider is key to consider when creating cell
Notes: ASK: “Why wouldn't we just have the operator take care of replenishing their materials, why have another position for this?” (answer: by the operator doing this, they will have to stop making products, travel to retrieve the parts and then travel back to their cell. This breaks the flow)

## Slide 40: Building Quality into the Cell
Objectives:
Define “poka-yoke” and “jidoka”, and review everyday examples
Identify the four levels of error-proofing
Identify and review prevention and detection examples of error-proofing
Define 7 steps to error-proofing a process
Discuss importance of developing a Line Stop Support Plan
Identify process improvements when error-proofing is not possible
Do’s and Don’ts of Cell Design
Building Quality into the Cell
Steps to Designing a Cell
Key Concepts of Cell Design
Notes: DO: Review section objectives on slide.

## Slide 41: Error-Proofing
Building Quality Into the Cell
Examples
Jidoka
Poka-Yoke
A Japanese term meaning, “mistake-proof”
A method of designing processes that will prevent errors
Also referred to as “autonomation”, means a method of transferring human intelligence to the process
The process detects abnormalities and stops when detected
Motion detect light switches room enter and exit
Car stops when object in path.
Auto shut-off irons
Automatic sinks in public restrooms
Low clearance barriers in parking garage
1
2
3
“Poka-Yoke” is the highest level of Jidoka
Notes: ASK: “What are other error proofing examples?”

## Slide 42: Error-Proofing
Building Quality Into the Cell
A
B
C
Ship
Level 4 - Perfect Quality Built In
Build in Quality
at Each Process
Rework
Scrap
Ship
Level 2 - End of Line Inspection
A
B
C
Inspection
A B C
Level 1 - Customer Inspects
Level 3 - End of Process Inspection
Notes: DO: Review the 4 levels of error proofing.
ASK: “What is wrong with stopping at Level 2? (we are waiting until after the 3rd process to check if we have a quality part… steps B and C could be working on defect (WASTE – and if they are working in batch even more so!)
SAY: “We want to reach a point where it is impossible to pass a defect onto the next process. In this section will discuss ways to build quality into the product so that we can achieve this.”

## Slide 43: Errors may either be prevented or detected
Technique | Prevention | Detection
Control (shut down) | An error is impossible | Defective item can’t move on to the next step
Warning | An error is about to be made | An error has been made
Building Quality Into the Cell
Notes: SAY: “With error-proofing we can implement a control/shut down technique in the process – with prevention an error would be impossible, with detection, the defect would be unable to move onto the next step.
By implementing a warning technique, prevention methods would allow us to know that an error is about to be made, and detection methods would let us know that an error has just occurred.”

## Slide 44: Control (Shutdown) Prevention and Detection Examples
Prevention
Access controlled by biometric scan
Vehicle won’t start unless in park and brake depressed.
Detection
Laundry dryers that have a device that shuts them down when overheating is detected
A computer spell checker
Building Quality Into the Cell
Reprinted with permission from BigPhotoStock.com
Notes: DO: Review examples.

## Slide 45: Warning Prevention and Detection Examples
Prevention
Warning systems in automobiles to alert driver that not all seatbelts have been fastened
Detection
Smoke detectors
Building Quality Into the Cell
Reprinted with permission from BigPhotoStock.com
Notes: DO: Review examples.

## Slide 46: Error-Proofing Contact Methods
Electrical outlets assure proper polarity – it is impossible to put a plug in the outlet incorrectly
Guide or guide pins that assure proper insertion
Magnetic contacts that assure proper positioning
Two handed start buttons to avoid hand accidents
Pressure sensitive mats that stop dangerous pinching machinery when someone steps onto the mat
Limit switches on fork trucks that prevent the truck from moving while the driver’s seat is unoccupied
Contact Methods
Building Quality Into the Cell
Reprinted with permission from BigPhotoStock.com
Notes: DO: Review examples.

## Slide 47: Error-Proofing Fixed Value Methods
If four labels from different rolls are needed on each shipping box, put all the labels on one roll to make it easy to spot missed labels
Kitting is having the exact amount of material needed for one unit in one box. Makes it easy to catch missing components
Sensors that count parts as they are placed in a box
Scales to weigh packaging documentation and alert an operator to a missed document
Fixed Value Methods
Building Quality Into the Cell
Reprinted with permission from BigPhotoStock.com
Notes: DO: Review examples.

## Slide 48: Error-Proofing Motion-Step Methods
Place photo-electric switches into each component bin. Beam must be broken on each bin before conveyor will move
Motion sensors to stop a machine to prevent safety errors
Motion-Step Methods
Building Quality Into the Cell
Reprinted with permission from BigPhotoStock.com
Notes: DO: Review examples.

## Slide 49: 7 Steps to Error-Proofing
Create a process map and identify the locations at which the defects are found and made
Evaluate current procedures for adequacy and determine if they are being followed
Identify defect provoking conditions at each process step
Identify the root cause(s) (error) of each type of defect and in which process step it occurs
Identify the type of error-proofing device required
Create the device and try it
Measure for effectiveness
Building Quality Into the Cell
Notes: DO: Review the seven steps.

## Slide 50: Develop a Line-Stop Support Plan
Establish line stop response assignments
Identify who does what when the line is stopped
Operators, Supervisors, Managers, etc.
Line-Stop Support Plan
Building Quality Into the Cell
Reprinted with permission from BigPhotoStock.com
Notes: SAY: “For detection methods and warning methods, it is important that a plan is in place and well practiced for what to do if the line needs to be stopped. Everyone needs to know who does what, and they need to be counted on to do their part so that the process can be trusted.”
ASK: “What happens in an andon environment when an operator flips the switch to red, and no one responds… he/she ultimately has to go get the supervisor…”

## Slide 51: When you can’t error-proof – Improve Visual Management.
Use colors and color-coding
  Filing
  Credit card receipts
Use shapes
  Notch a stack of forms so it is easy to tell if forms are out of order
Make it easy to do it right
  Checklists
  Effective data collection formats
  Workflow with fewer hand-offs
  Symbols
Building Quality Into the Cell
Reprinted with permission from BigPhotoStock.com
Notes: SAY: “Error-proofing is not always possible given the process or what can be reasonably implemented during the improvement period. This slide shows some great ideas for making the process “better” in these instances.”
SAY: “With each of these examples, is it possible to pass on a defect? Yes. However, the chances are much less.”

## Slide 52: Error-Proofing Summary
Error-Proofing devices can
  Prevent errors from occurring
  Detect the error after it occurred
  Detect the defect after it has been made
The best error-proofing devices are
  Simple and cheap
  Part of the regular process
  Close to where the error is made
Building Quality Into the Cell
Notes: DO: Review summary points.

## Slide 53: The “Do’s and Don’ts” of Cell Design
Objectives:
Review and discuss each of the Do’s and Don’ts of Cell Design
Complete review of key learnings from Cell Design
Do’s and Don’ts of Cell Design
Building Quality into the Cell
Steps to Designing a Cell
Key Concepts of Cell Design
Notes: OPTIONAL EXERCISE:
PURPOSE: To provide an interactive experience for the learners to help remember the Do’s and Don’ts of Cell Design.
MATERIALS NEEDED: Markers and chartpaper
DO: Break the class into small groups and divvy up each of the “do’s and don’ts”. Ideally you could assign each slide to a different table or group.
INSTRUCTIONS: Each table or group must come up with an icon, drawing, or graphic that represents that particular principle. Have them draw this on a chart paper with markers and report out to the rest of the group. Set a brief time limit to encourage creativity (plus the time crunch makes it more fun!). Recommended no more than 5 minutes.
DO: As you review each of the drawings, take that time to really discuss what is meant by this principle with the group.

## Slide 54: The “Do’s and Don’ts” of Cell Design
DO | DON’T
Bring the part back to the operator | Design one-way machines
Keep height of all items in the workplace very low | Avoid waste of motion and any potentially unsafe reaching
Ask “why” and challenge what may have always been traditionally accepted | Assume that you need to limited by using certain machines
Use ideas | Unnecessarily use money
Do’s and Don’ts of Cell Design
Notes: DO: Discuss each in detail.

## Slide 55: The “Do’s and Don’ts” of Cell Design
DO | DON’T
Use equipment to permit one unit flow | Think in terms of batching
Utilize safe and easy-to- service machines and equipment | Utilize old, outdated machines that may be potentially unsafe or difficult to service
Think “flexible” and “responsible” machines | Don’t think “super-machines” or “all-in-one machines”
Think one-piece flow | Think batch production
Do’s and Don’ts of Cell Design
Notes: DO: Discuss each in detail.

## Slide 56: The “Do’s and Don’ts” of Cell Design
DO | DON’T
Add value to the product continuously through the process | Incorporate waste into the process
Think “bare bones” and add options when necessary | Incorporate machines with unneeded accessories
Get your hands dirty! | Be a catalog engineer!
Design machines to be narrow, deep and closely spaced together | Design machines with wide frontages spread far apart
Do’s and Don’ts of Cell Design
Notes: DO: Discuss each in detail.

## Slide 57: The “Do’s and Don’ts” of Cell Design
DO | DON’T
Make machines easy to detach and relocate | Do not design machines with “roots and vines”
Use shuttles to allow throw-in loading with auto-ejection (hanedashi) | Loose sight of opportunities to eliminate non-value added activities for the operator
Do’s and Don’ts of Cell Design
Notes: DO: Discuss each in detail.

## Slide 58: Review Exercise
2 Minute Review
In pairs, or in small groups, spend 5 minutes discussing key learnings and take-aways from this Cell Design Event thus far
One person from each group will share one learning that was discussed with the rest of the class
Do’s and Don’ts of Cell Design

## Slide 59
Other Modules In This Series:
5S
Standard Work
Total Productive Maintenance (TPM)
Administrative Lean
Cell Design/ Production Preparation Process (3P)
Kaizen
Kanban
Problem Solving
Poka Yoke Quality Systems
Transaction Process Improvement (TPI)
Cause & Effect Diagram with the Additions of Cards (CEDAC)
Single Minute Exchange of Dies (SMED)
Value Stream Mapping (VSMi®)
Visual Management
Managing Daily Process Excellence
For More Information Please Contact:
Mark DeLuzio, President and CEO
+1.860.234.0915
mark.deluzio@leanhorizons.com
Strategically Creating Value Through the Elimination of Waste