## Slide 1: Exercise: Rusty’s Wrench
Create an accurate Current State Value Stream Map from case study example data.
Objective
Instructions
Read through the case study data handout for Rusty’s Wrench. Make notes where needed.
In small groups, create the Current State Map
using chart paper and post-it notes.
NOTE: KEEP YOUR COMPLETED MAP FOR LATER EXERCISE
Time to Complete
Deliverable
40 minutes
One person from each group will present map to the class.
Comments and feedback encouraged.
Create Current State Map
Notes: DO: Pass out flip chart paper, markers, calculators, and post-it notes. Pass out the Data Sheet Handouts for Rusty’s Wrench. Read the instructions of the exercise. They are to complete the Current State Map in small groups.
DO: Emphasize after the exercise that they will need these maps for a later exercise – do not discard or erase.

## Slide 2: Case Study Example: Rusty’s Wrench
Background
  Rusty’s Wrench Factory produces several types of wrenches and is the sole supplier to Giant Tool Supply, the nation’s largest supplier of tools to the industrial community. Rusty produces metric and SAE sizes of open-end wrenches.
Customer Requirements
  3,200 sets per month: 2,200 SAE/1,000 metric
  Customer operates on one shift
  Wrenches are packed in sets of 25
  The customer orders by sets
  Rusty’s Wrench provides a daily shipment by truckload to Giant Tool Supply
Rusty’s Wrench Work Time
  20 days in a month
  Two shift operation in all departments
  Eight (8) hour shifts
  Two 10- minute breaks during each shift, 10- minute cleanup allowed during each shift, unpaid lunch
Create Current State Map
Notes: HANDOUT

## Slide 3: Case Study Example: Rusty’s Wrench
Production Processes
  Rusty’s process begins with hot forging (drop forge) a wrench, followed by machining, polishing, plating, and packing into sets. The sets are then staged and shipped to Giant Tool Supply on a daily basis.
  Changing over between SAE and Metric requires 1 hour changeover in Forging, and 20 minutes in Machining
  Steel bar stock is supplied by Lean Steel Company, delivering twice a week on Monday and Thursday
Rusty’s Production Control Department
  Receives Giant’s 90/60/30 day forecast and enters into MRP
  Issues an 8 week forecast to Lean Steel via MRP
  Releases for cut bar stock via weekly faxed orders to Lean Steel
  Receives daily firm order from Giant Tool Supply
  Generates weekly MRP-based build schedules to all manufacturing departments
  Issues daily shipping schedule to Shipping Department
Create Current State Map
Notes: HANDOUT

## Slide 4: Rusty’s Wrench Factory – Data Set
Create Current State Map
Manual Drop Forge Press and Trimming. Process includes trim after forge. (6 operators) | Manual process w/continuously running machines.Needs to be processed thru 6 machines. (6 operators) | Manual polish operation. Operator relies on visual inspection of parts. (1 operator) | Parts are manually hung on a rack and processed through the plating process. (5 operators) | Operators manually pack wrenches into sets. (2 operators) | Removes sets from Pack and stages for daily truck shipment to the customer.
DOI = 12“ Proc Time = 12” | DOI = 12“ Proc Time = 12” | DOI = 10“ Proc Time = 10” | DOI = 16“ Proc Time = 90’ | (Per Set) DOI = 225“ Proc Time = 450” | N/A
I Hour from SAE to Metric | 20 Minutes (entire cell) | None | None | None | N/A
100 % | 98% | 99% | 99% | N/A | N/A
95%, all rejected parts are scrapped. | 98% first pass, most parts can be reworked. | 94% first pass, most parts can be reworked | 98% first pass, most parts can be reworked | 99.5% first pass | N/A
6000 pcs of cut bar stock before forge. 18000 after forge (12k SAE, 6k Metric) | 25000 units: 18k SAE, 7k Metric | 55000 units: 35k SAE, 20k Metric | 6000 units All SAE | 75000 units 50k SAE 25k Metric | None – just daily ship quantities.
Forge
Machine
Polish
Plate
Pack
Ship
Operation
Description
DOI Observed &
Processing Time
Changeover
Machine
Reliability
Quality
Inventory
Notes: Explain that this chart summarizes the key data points and can be used to help map out the current state.
This data is the result of observation and data-gathering activity.
Note: Pause here and allow students to work in teams to create their maps – the following slides are the Answers

## Slide 5: Rusty’s Wrench Factory – TAKT Time
TAKT Time - How often you should produce one part, based on the rate of sales to meet customer requirements.
Calculation
Example
  1 shift x 8hrs 28,800 seconds
  2 - 10 min breaks / shift - 1,200 seconds
  1 - 10 min cleanup /shift - 600 seconds
  Available working time = 27,000 seconds
  Customer demand /month 3,200 sets/month
  20 days/month x 2 shifts = 3,200 ÷ 40 = 80 sets
  Sets required per shift = 80 sets
  25 pieces in a set = 80 sets x 25 pcs/set
  Pieces required per shift = 2,000 pieces
Create Current State Map
Available working time
Customer demand (units)
27,000 seconds
2,000 pieces
= 13.5 seconds
=
Notes: Reinforce the importance of Takt time to VSM in understanding demand.
Review the calculation, based on Rusty’s Wrench Factory example.

## Slide 6: Case Study Example: Rusty’s Wrench
Create Current State Map
450 sec
1.5 days
5400 sec (or 90 min)
13.8 days
10 sec
6.3 days
12 sec
4.5 days
12 sec
1.5 days
Demand = 3200 sets/mo
2200 SAE, 1000 Metric
2 Shifts
Set = 25 pcs
Production L.T. = 46.4 days
Proc. Time = 5884 sec (or 98 min)
I
= 6
Machine
DOI = 12”
C/O Time = 20’
Uptime = 98%
Quality = 98%
= 1
Polish
DOI = 10”
C/O Time = n/a
Uptime = 99%
Quality = 94%
Lean Steel
Giant Tool
Rusty’s Wrench Current State Map
I
I
I
2X Mon & Thurs
Daily
27,000 Seconds
2,000 Pieces
Takt Time
= 13.5 seconds
Weekly
Fax
Daily Orders
MRP
System
Production Control
Daily Ship
Schedule
(Paper)
6,000 Cut Bars
18,000
12k SAE
6k Metric
25,000
18k SAE
7k Metric
55,000
35k SAE
20k Metric
= 6
Forge
DOI = 12”
C/O Time = 60”
Uptime = 100%
Quality = 95%
90/60/30 Forecast
Plate
= 5
DOI = 16”
C/O Time = n/a
Uptime = 99%
Quality = 98%
I
6,000
6k SAE
0 Metric
Pack
= 2
DOI = 225” (set of 25)
C/O Time = n/a
Uptime = n/a
Quality = 99.5%
I
75,000
50k SAE
25k Metric
Ship
18.8 days
Weekly Build Schedules

## Slide 7: Exercise
Create a marked-up Current State Map for Rusty’s Wrench.
Objective
Instructions
In teams, mark-up your Current State Map using RED marker. Use the questions provided in sequence in this chapter as your guide.
Time to Complete
Deliverable
15 minutes
One person from the team will present the map to the class.
Comments and feedback will be encouraged.
Interrogating the Current State
Notes: SAY: “Now we will repeat this exercise again in your small groups for Rusty’s Wrench. Please take 10 minutes to review your current state maps and mark up with improvement opportunities. Use the Interrogation Questions (in order) on the slide as your guide.”

## Slide 8: Case Study Example: Rusty’s Wrench Marked-Up Current State
Interrogating the Current State
450 sec
1.5 days
5400 sec (or 90 min)
13.8 days
10 sec
6.3 days
12 sec
4.5 days
12 sec
1.5 days
Demand = 3200 sets/mo
2200 SAE, 1000 Metric
2 Shifts
Set = 25 pcs
Production L.T. = 46.4 days
Proc. Time = 5884 sec (or 98 min)
I
= 6
Machine
DOI = 12”
C/O Time = 20’
Uptime = 98%
Quality = 98%
= 1
Polish
DOI = 10”
C/O Time = n/a
Uptime = 99%
Quality = 94%
Lean Steel
Giant Tool
Rusty’s Wrench Current State Map
I
I
I
2X Mon & Thurs
Daily
27,000 Seconds
2,000 Pieces
Takt Time
= 13.5 seconds
Weekly
Fax
Daily Orders
MRP
System
Production Control
Daily Ship
Schedule
(Paper)
6,000 Cut Bars
18,000
12k SAE
6k Metric
25,000
18k SAE
7k Metric
55,000
35k SAE
20k Metric
= 6
Forge
DOI = 12”
C/O Time = 60”
Uptime = 100%
Quality = 95%
90/60/30 Forecast
Plate
= 5
DOI = 16”
C/O Time = n/a
Uptime = 99%
Quality = 98%
I
6,000
6k SAE
0 Metric
Pack
= 2
DOI = 225” (set of 25)
C/O Time = n/a
Uptime = n/a
Quality = 99.5%
I
75,000
50k SAE
25k Metric
Ship
18.8 days
Weekly Build Schedules
Improve
Quality
Improve
Quality
Reduce
Changeover
1 pc Flow
1 pc Flow
Reduce
DOI

## Slide 9: Case Study Example: Rusty’s Wrench Future State Map
Interrogating the Current State
Machine & Polish
8 sec
5400 sec (or 90 min)
2 days
1 day
22 sec
2 days
12 sec
1.5 days
Demand = 3200 sets/mo
2200 SAE, 1000 Metric
2 Shifts
Set = 25 pcs
Production L.T. = 6.5 days
Proc. Time = 5442 sec (or 90’ 42”)
= 7
DOI = 12”
C/O Time = 20’
Uptime = 98%
Quality = 98%
Lean Steel
Giant Tool
Rusty’s Wrench Future State Map
2X Mon & Thurs
Daily
27,000 Seconds
2,000 Pieces
Takt Time
= 13.5 seconds
Weekly
Fax
Daily Orders
MRP
System
Production Control
Daily Ship
Schedule
(Paper)
= 6
Forge
DOI = 12”
C/O Time = 60”
Uptime = 100%
Quality = 95%
90/60/30 Forecast
Plate
= 5
DOI = 16”
C/O Time = n/a
Uptime = 99%
Quality = 98%
Pack & Ship
= 3
DOI = 225” (set of 25)
C/O Time = n/a
Uptime = n/a
Quality = 99.5%
Improve
Quality
Improve
Quality
Reduce
Changeover
1.5 Days
2 Days
1 Day
2 Days unpacked finished goods
Signal
1 Hour
250
250
1 Hour
250
1 Hour
250
1 Hour
500
1 Hour
250
Reduce
DOI