## Slide 1: Case Study Example: Rusty’s Wrench
Background
  Rusty’s Wrench Factory produces several types of wrenches and is the sole supplier to Giant Tool Supply, the nation’s largest supplier of tools to the industrial community. Rusty produces metric and SAE sizes of open-end wrenches.
Customer Requirements
  3,200 sets per month: 2,200 SAE/1,000 metric
  Customer operates on one shift
  Wrenches are packed in sets of 25
  The customer orders by sets
  Rusty’s Wrench provides a daily shipment by truckload to Giant Tool Supply
Rusty’s Wrench Work Time
  20 days in a month
  Two shift operation in all departments
  Eight (8) hour shifts
  Two 10- minute breaks during each shift, 10- minute cleanup allowed during each shift, unpaid lunch
Create Current State Map
Notes: HANDOUT

## Slide 2: Case Study Example: Rusty’s Wrench
Production Processes
  Rusty’s process begins with hot forging (drop forge) a wrench, followed by machining, polishing, plating, and packing into sets. The sets are then staged and shipped to Giant Tool Supply on a daily basis.
  Changing over between SAE and Metric requires 1 hour changeover in Forging, and 20 minutes in Machining
  Steel bar stock is supplied by Lean Steel Company, delivering twice a week on Monday and Thursday
Rusty’s Production Control Department
  Receives Giant’s 90/60/30 day forecast and enters into MRP
  Issues an 8 week forecast to Lean Steel via MRP
  Releases for cut bar stock via weekly faxed orders to Lean Steel
  Receives daily firm order from Giant Tool Supply
  Generates weekly MRP-based build schedules to all manufacturing departments
  Issues daily shipping schedule to Shipping Department
Create Current State Map
Notes: HANDOUT

## Slide 3: Rusty’s Wrench Factory – Data Set
Create Current State Map
Manual Drop Forge Press and Trimming. Process includes trim after forge. (6 operators) | Manual process w/continuously running machines.Needs to be processed thru 6 machines. (6 operators) | Manual polish operation. Operator relies on visual inspection of parts. (1 operator) | Parts are manually hung on a rack and processed through the plating process. (5 operators) | Operators manually pack wrenches into sets. (2 operators) | Removes sets from Pack and stages for daily truck shipment to the customer.
DOI = 12“ Proc Time = 12” | DOI = 12“ Proc Time = 12” | DOI = 10“ Proc Time = 10” | DOI = 16“ Proc Time = 90’ | (Per Set) DOI = 225“ Proc Time = 450” | N/A
I Hour from SAE to Metric | 20 Minutes (entire cell) | None | None | None | N/A
100 % | 98% | 99% | 99% | N/A | N/A
95%, all rejected parts are scrapped. | 98% first pass, most parts can be reworked. | 94% first pass, most parts can be reworked | 98% first pass, most parts can be reworked | 99.5% first pass | N/A
6000 pcs of cut bar stock before forge. 18000 after forge (12k SAE, 6k Metric) | 25000 units: 18k SAE, 7k Metric | 55000 units: 35k SAE, 20k Metric | 6000 units All SAE | 75000 units 50k SAE 25k Metric | None – just daily ship quantities.
Forge
Machine
Polish
Plate
Pack
Ship
Operation
Description
DOI Observed &
Processing Time
Changeover
Machine
Reliability
Quality
Inventory
Notes: Explain that this chart summarizes the key data points and can be used to help map out the current state.
This data is the result of observation and data-gathering activity.
Note: Pause here and allow students to work in teams to create their maps – the following slides are the Answers